## Slide 1
PREDICTIVE MAINTENANCE
Enterprise Predictive Maintenance &
Industrial Equipment Failure Intelligence
Case Study ML-004 · Model Evaluation & Technical Presentation
Ezitech Engineering Framework Internship · Team of 2 ML Engineers · 4-Week Sprint

## Slide 2
THE PROBLEM
Fixed maintenance schedules are costing the factory floor
1
Unplanned Downtime
Machines fail between scheduled checks, halting production lines without warning.
2
High Maintenance Cost
Fixed-interval servicing replaces parts that still have useful life left.
3
Poor Spare-Parts Planning
No forecast of which parts will be needed, or when.
4
No Real-Time Visibility
1,200 engineers across 45 factories have no live view of equipment health.
Goal: Move from fixed-interval to condition-based maintenance using live sensor data — predict failures before they happen.
02

## Slide 3
THE DATA
24,042 sensor readings across a 20-machine fleet
24,042
Sensor readings
20
Machines, 4 types
9
Sensor channels
14.8%
Failure rate (24h)
Sensor channels
Vibration RMS
Motor Temperature
Current
Pressure Level
RPM
Ambient Temp
Humidity
Voltage
Machine Load
Two prediction targets
rul_hours — continuous, Remaining Useful Life
failure_within_24h — binary, 24-hour failure alert
2-4% missing values per sensor (dropout) — imputed per-machine via forward/backward fill
03

## Slide 4
SYSTEM DESIGN
End-to-end pipeline architecture
Sensor
Ingestion
CSV / streaming
IoT data
Feature
Engineering
38 engineered
features
Equipment
Health Engine
XGBoost RUL +
Failure models
Explainability
& MLOps
SHAP, MLflow,
drift checks
Serving
Layer
FastAPI +
Dashboard
Backend stack: Python · FastAPI · (PostgreSQL + Redis planned for production scale)
Outputs per machine, per reading:
Health Score
0-100
Failure Probability
24h window
RUL
hours
Recommendation
5 action tiers
04

## Slide 5
FEATURE ENGINEERING
From raw sensor stream to a 38-feature matrix
Rolling mean & std (6-reading window) — vibration, temp, current, pressure, RPM
Trend slope — local linear degradation direction for vibration & temperature
Vibration energy (RMS²) — standard severity measure
Temperature gradient — motor temp minus ambient
Utilization rate & operating hours since last service
Cumulative prior failures per machine
Maintenance interval bucket — recent / moderate / overdue / critical
One-hot encoded machine type & operating mode
Leakage-safe imputation: missing sensor values (2-4% per channel) filled per-machine via forward/backward fill, median fallback.
05

## Slide 6
EQUIPMENT HEALTH ENGINE · MODEL 1
Remaining Useful Life — XGBoost Regression
MAE
17.8 hrs
RMSE
23.3 hrs
R²
0.263
Machine-level train/test split (15 vs. 5 machines) — no machine's readings appear in both sets, giving an honest read on unseen equipment.
06

## Slide 7
EQUIPMENT HEALTH ENGINE · MODEL 2
24-Hour Failure Classification — XGBoost
ROC-AUC
0.987
Recall
94.6%
Precision
58.8%
Tuned for recall over precision
A missed failure costs far more than a false alarm — class-weighting catches 94.6% of true failures at the cost of some extra inspections.
07

## Slide 8
EXPLAINABLE AI
What drives each prediction — SHAP analysis
Top failure-risk drivers
Cumulative prior failures
Machines with a failure history are flagged as higher risk
Rolling motor temperature
Sustained heat is a classic pre-failure signal
Hours since maintenance
Overdue service time raises risk sharply
These per-prediction explanations feed the dashboard's “Top Risk Factors” panel for engineers.
08

## Slide 9
DECISION LAYER
Maintenance Recommendation Engine
Emergency
Shutdown
Fail prob ≥ 80% or
Health < 20
Immediate
Repair
Fail prob ≥ 50% or
Health < 40
Scheduled
Maintenance
Fail prob ≥ 25% or
Health < 60
Continue
Monitoring
Health < 80
Normal
Operation
Health ≥ 80
Failure Risk Heatmap (test fleet)
Every prediction from the API maps directly to one of these five tiers — turning a probability into an action an engineer can execute immediately.
09

## Slide 10
MLOPS
Production-readiness beyond the notebook
1
Experiment Tracking
Both models logged to MLflow — params, metrics, and artifacts versioned per run.
2
Model Registry
Trained models persisted as versioned artifacts alongside their feature schema for reproducible inference.
3
Sensor Drift Detection
Recent vs. overall feature-mean comparison flags shifts beyond a 15% threshold per sensor.
4
CI Pipeline
GitHub Actions runs the full test suite and a pipeline smoke-test on every push.
10

## Slide 11
SERVING LAYER
Prediction API & Operations Dashboard
FastAPI — POST /predict
POST /predict
{
"vibration_rms": 4.2,
"temperature_motor": 95,
"hours_since_maintenance": 580,
...
}
→ 200 OK
{
"health_score": 6.8,
"failure_probability": 0.9668,
"predicted_rul_hours": 51.4,
"recommendation": "Emergency Shutdown"
}
Streamlit Operations Dashboard
Fleet-wide risk table, color-coded by health score
Per-machine drill-down with health trend
Live “what-if” predictor for manual sensor entry
Health-by-machine-type comparison view
streamlit run src/dashboard.py
11

## Slide 12
BUSINESS IMPACT & NEXT STEPS
From condition-based maintenance to fleet-wide savings
Reduced unplanned downtime
Extended equipment lifespan
Smarter spare-parts planning
Earlier safety intervention
Next steps for the team
Cost-based threshold tuning once false-alarm cost is known precisely
LSTM sequence model on raw sensor windows to lift RUL R²
Multi-factory validation across the full 18,000-machine fleet
PostgreSQL + Redis for live reading persistence and prediction caching
Thank you — questions welcome